## Slide 1: Course: Digital Logic Design
Number System
Decimal
Binary
Hexa Decimal
Octal
Addition / Subtraction
Multiplication / Division
How Computer Add or Subtract
Gates
Boolean Algebra
types of Boolean Algebra
K-Map
etc
Circuits
Combinational Circuit
Can't store Data
Sequential Circuit
Can store Data

## Slide 2: Number System
It is Basically a system in which we able to know how to express a Number and how to deal with the Number.
Add / Sub / Multiplication / Division
How to convert a number from one system to another
etc.

## Slide 3: Number Systems
1
Decimal Number
Base 10
2
Binary Numbers
Base 2
3
Octal Number
Base 8
4
Hexadecimal Number
Base 16

## Slide 4: Decimal Number System
Definition:
It is a standard number system used to represent integers and non-integer numbers.
This is the number system we use in daily life.
Digits:
0
1
2
3
4
5
6
7
8
9
Base (Radix): 10
Representation:
(375)₁₀
(25.75)₁₀
(100)₁₀
(13.625)₁₀

## Slide 5: Binary Number System
Definition:
Binary is the language of computers. It uses only two digits.
It's used to store, access, and manipulate data in computers.
Digits:
0
1
Base (Radix): 2
Representation:
(101110111)₂
(11001)₂
(101101)₂
(1101.101)₂

## Slide 6: Octal Number System
Definition:
Octal number system uses 8 digits. One octal digit represents exactly 3 binary bits.
It is convenient for representing binary numbers in shorter form.
Digits:
0
1
2
3
4
5
6
7
Base (Radix): 8
Representation:
(567)₈
(144)₈
(31.6)₈
(113.2)₈

## Slide 7: Hexadecimal Number System
Definition:
Hexadecimal uses 16 symbols. One hex digit represents exactly 4 binary bits.
Widely used in memory addresses, color codes, and debugging.
Digits & Characters:
0
1
2
3
4
5
6
7
8
9
A
B
C
D
E
F
A=10 B=11 C=12 D=13 E=14 F=15
Base (Radix): 16
Representation:
(177)₁₆
(FF)₁₆
(17D)₁₆
(2D.4)₁₆

## Slide 8: CONVERSIONS
Decimal → Binary / Octal / Hexadecimal
Binary / Octal / Hexadecimal → Decimal

## Slide 9: DECIMAL TO BINARY CONVERSION
(375)₁₀ → Binary
2
375
2
187
1
2
93
1
2
46
1
2
23
0
2
11
1
2
5
1
2
2
1
1
0
Read remainders
bottom → top
Answer: (101110111)₂

## Slide 10: DECIMAL TO BINARY CONVERSION
(25)₁₀ → Binary
2
25
2
12
1
2
6
0
2
3
0
2
1
1
0
1
Read remainders
bottom → top
Answer: (11001)₂

## Slide 11: DECIMAL TO BINARY CONVERSION
(45)₁₀ → Binary
2
45
2
22
1
2
11
0
2
5
1
2
2
1
1
0
Read remainders
bottom → top
Answer: (101101)₂

## Slide 12: DECIMAL TO BINARY CONVERSION
(100)₁₀ → Binary
2
100
2
50
0
2
25
0
2
12
1
2
6
0
2
3
0
1
1
Read remainders
bottom → top
Answer: (1100100)₂

## Slide 13: DECIMAL TO BINARY CONVERSION
(13)₁₀ → Binary
2
13
2
6
1
2
3
0
2
1
1
0
1
Read remainders
bottom → top
Answer: (1101)₂

## Slide 14: DECIMAL TO BINARY (with Point)
(75.25)₁₀ → Binary
Integer Part
2
75
2
37
1
2
18
1
2
9
0
2
4
1
2
2
0
1
0
Fractional Part
0.25 × 2 = 0.50
→
0
0.50 × 2 = 1.00
→
1
top → bottom
Answer: (1001011.01)₂

## Slide 15: DECIMAL TO BINARY (with Point)
(13.625)₁₀ → Binary
Integer: 13 → 1101₂
Fractional:
0.625 × 2 = 1.25
→
1
0.25 × 2 = 0.50
→
0
0.50 × 2 = 1.00
→
1
Answer: (1101.101)₂

## Slide 16: DECIMAL TO OCTAL CONVERSION
(375)₁₀ → Octal
8
375
8
46
7
8
5
6
0
5
Answer: (567)₈

## Slide 17: DECIMAL TO OCTAL CONVERSION
(100)₁₀ → Octal
8
100
8
12
4
8
1
4
0
1
Answer: (144)₈

## Slide 18: DECIMAL TO OCTAL CONVERSION
(50)₁₀ → Octal
8
50
8
6
2
0
6
Answer: (62)₈

## Slide 19: DECIMAL TO OCTAL (with Point)
(75.25)₁₀ → Octal
Integer Part
8
75
8
9
3
1
1
Fractional Part
0.25 × 8 = 2.00
→
2
top → bottom
Answer: (113.2)₈

## Slide 20: DECIMAL TO OCTAL (with Point)
(25.75)₁₀ → Octal
Integer: 25 → 31₈
Fractional:
0.75 × 8 = 6.00
→
6
Answer: (31.6)₈

## Slide 21: DECIMAL TO HEXADECIMAL CONVERSION
(381)₁₀ → Hexadecimal
16
381
16
23
13 (D)
1
7
Hex
Decimal
A
10
B
11
C
12
D
13
E
14
F
15
Answer: (17D)₁₆

## Slide 22: DECIMAL TO HEXADECIMAL CONVERSION
(255)₁₀ → Hexadecimal
16
255
16
15
15 (F)
0
15 (F)
Hex
Decimal
A
10
B
11
C
12
D
13
E
14
F
15
Answer: (FF)₁₆

## Slide 23: DECIMAL TO HEXADECIMAL CONVERSION
(100)₁₀ → Hexadecimal
16
100
16
6
4
0
6
Answer: (64)₁₆

## Slide 24: DECIMAL TO HEXADECIMAL CONVERSION
(375)₁₀ → Hexadecimal
16
375
16
23
7
1
7
Answer: (177)₁₆

## Slide 25: DECIMAL TO HEXADECIMAL (with Point)
(76.25)₁₀ → Hexadecimal
Integer: 76 → 4C₁₆
16
76
16
4
12 (C)
0
4
Fractional:
0.25 × 16 = 4.00
→
4
Hex
Decimal
A
10
B
11
C
12
D
13
E
14
F
15
Answer: (4C.4)₁₆

## Slide 26: DECIMAL TO HEXADECIMAL (with Point)
(45.25)₁₀ → Hexadecimal
Integer: 45 → 2D₁₆
16
45
16
2
13 (D)
0
2
Fractional:
0.25 × 16 = 4.00
→
4
Hex
Decimal
A
10
B
11
C
12
D
13
E
14
F
15
Answer: (2D.4)₁₆

## Slide 27: Binary → Decimal | (1101.101)₂
Position :
Binary :
3
1
2
1
1
0
0
1
.
.
–1
1
–2
0
–3
1
Value:
1×(2)³
+
1×(2)²
+
0×(2)¹
+
1×(2)⁰
+
1×(2)⁻¹
+
0×(2)⁻²
+
1×(2)⁻³
8 + 4 + 0 + 1 + 0.5 + 0 + 0.125 = (13.625)₁₀

## Slide 28: Binary → Decimal | (1011.11)₂
Position :
Binary :
3
1
2
0
1
1
0
1
.
.
–1
1
–2
1
Value:
1×(2)³
+
0×(2)²
+
1×(2)¹
+
1×(2)⁰
+
1×(2)⁻¹
+
1×(2)⁻²
8 + 0 + 2 + 1 + 0.5 + 0.25 = (11.75)₁₀

## Slide 29: Binary → Decimal | (1110.01)₂
Position :
Binary :
3
1
2
1
1
1
0
0
.
.
–1
0
–2
1
Value:
1×(2)³
+
1×(2)²
+
1×(2)¹
+
0×(2)⁰
+
0×(2)⁻¹
+
1×(2)⁻²
8 + 4 + 2 + 0 + 0 + 0.25 = (14.25)₁₀

## Slide 30: Binary → Decimal | (1101)₂
Position :
Binary :
3
1
2
1
1
0
0
1
Value:
1×(2)³
+
1×(2)²
+
0×(2)¹
+
1×(2)⁰
8 + 4 + 0 + 1 = (13)₁₀

## Slide 31: Binary → Decimal | (10110)₂
Position :
Binary :
4
1
3
0
2
1
1
1
0
0
Value:
1×(2)⁴
+
0×(2)³
+
1×(2)²
+
1×(2)¹
+
0×(2)⁰
16 + 0 + 4 + 2 + 0 = (22)₁₀

## Slide 32: Octal → Decimal | (567.4)₈
Value:
5×(8)²
+
6×(8)¹
+
7×(8)⁰
+
4×(8)⁻¹
320 + 48 + 7 + 0.5 = (375.5)₁₀

## Slide 33: Octal → Decimal | (144.2)₈
Value:
1×(8)²
+
4×(8)¹
+
4×(8)⁰
+
2×(8)⁻¹
64 + 32 + 4 + 0.25 = (100.25)₁₀

## Slide 34: Octal → Decimal | (31.6)₈
Value:
3×(8)¹
+
1×(8)⁰
+
6×(8)⁻¹
24 + 1 + 0.75 = (25.75)₁₀

## Slide 35: Hexadecimal → Decimal | (177.A)₁₆
Value:
1×(16)²
+
7×(16)¹
+
7×(16)⁰
+
10×(16)⁻¹
256 + 112 + 7 + 0.625 = (375.625)₁₀
Hex
Decimal
A
10
B
11
C
12
D
13
E
14
F
15

## Slide 36: Hexadecimal → Decimal | (FF.8)₁₆
Value:
15×(16)¹
+
15×(16)⁰
+
8×(16)⁻¹
240 + 15 + 0.5 = (255.5)₁₀
Hex
Decimal
A
10
B
11
C
12
D
13
E
14
F
15

## Slide 37: Hexadecimal → Decimal | (2D.4)₁₆
Value:
2×(16)¹
+
13×(16)⁰
+
4×(16)⁻¹
32 + 13 + 0.25 = (45.25)₁₀
Hex
Decimal
A
10
B
11
C
12
D
13
E
14
F
15